## Slide 1: Introduction
John m. Hochwalt, pe, se
Kpff consulting engineers, seattle

## Slide 2: The Masonry Society
  is an educational, scientific, and technical society dedicated to the advancement of scientific, engineering, architectural, and construction knowledge of masonry.
  My Roles:
  Chair of the Seismic and Limit Design Subcommittee for TMS 402/602
  Voting member of the TMS 402/602
  Board of Director's Representative for Zone 1

## Slide 3: The Masonry Society

## Slide 4: The Masonry Society
  My Goals for Today:
  Give an informative and interesting presentation
  Learn from all of you
    What challenges do you face in designing masonry in Hawaii?
    Are there ways in which existing codes and standards miss the mark in your practices?
    How could TMS better provide information to meet your needs.

## Slide 5: Masonry Veneers
Anchored and adhered

## Slide 6: Outline
Introduction to Veneer
Anchored Veneers
Adhered Veneers

## Slide 7: Introduction to Veneer

## Slide 8: Introduction to Veneer
  What is a veneer?
  What types of veneer are there?
  Components of veneers
    Anchored veneer
    Adhered veneer

## Slide 9: What is a veneer?
2018 IBC:
Veneer: A facing attached to a wall for the purpose of providing ornamentation, protection, or insulation, but not counted as adding strength to the wall.
TMS 402-16:
Veneer, masonry: A masonry wythe that provides the exterior finish of a wall system and transfers out-of-plane load directly to a backing, but is not considered to add strength or stiffness to the wall system.
4/12/2022
Introduction to Veneer
9

## Slide 10: Anchored Veneer
2018 IBC
Veneer secured with approved mechanical fasteners to an approved backing.
Image from imiweb.org

## Slide 11: Adhered Veneer
IBC
Veneer secured and supported through the adhesion of an approved bonding material applied to an approved backing.
Image from imiweb.org

## Slide 12: Structural Masonry Veneer
Reinforced masonry wall, typically designed to deliver wind and seismic loads directly to structure. Backing provides support for sheathing, air barrier and insulation, but not masonry.
Allows panelization
Limited connections
High performance
Image from wscpa.org

## Slide 13: Anchored Veneer

## Slide 14: Agenda
Behavior of Anchored Veneers
Code Requirements
Prescriptive Design
Alternative Design
  Full Engineered Method
  Tributary Area Method

## Slide 15: What do we want to know?
  How does the anchored veneer behave as a system?
  What criteria should we use to assess veneer behavior?
4/12/2022
Behavior of Anchored Veneer
15

## Slide 16: Behavior of Anchored Veneers
Image from imiweb.org
4/12/2022
Behavior of Anchored Veneer
16

## Slide 17: Behavior of Components
Behavior of Components
Masonry
  High stiffness, low strength
  Will Crack
Anchors and Backing
  Elastic
Masonry
Anchors
Backing
4/12/2022
Behavior of Anchored Veneer
17

## Slide 18: Initial Behavior
Load
  Biggest pressure differential across veneer
Masonry
  Masonry stiffest element
  Load stays in veneer
Anchors
  Load transferred at top and bottom anchors
4/12/2022
Behavior of Anchored Veneer
18

## Slide 19: Behavior at Service Loads
Masonry
  Masonry cracks
Anchors
  Load transferred at top and bottom anchors and anchors adjacent to cracks
4/12/2022
Behavior of Anchored Veneer
19

## Slide 20: Service Load Criteria
Limit Ingress of Water
Limit Crack Width
=2
4/12/2022
Behavior of Anchored Veneer
20

## Slide 21: Service Load Criteria
Suggested maximum crack width:
  0.04” (WSCPA)
  0.05” (Clark and Fried)
Suggested veneer deflection limit:
4/12/2022
Behavior of Anchored Veneer
21

## Slide 22: Service Load Criteria
How stiff should backing be to limit crack width?
where is the “stretch” of the anchor
4/12/2022
Behavior of Anchored Veneer
22

## Slide 23: Service Load Criteria
Anchor Displacement
Suggested allowances for anchor displacement, Da:
  Adjustable: 1/16” free play + 1/16” = 1/8”
  Wire: 0”
  Corrugated: 3/16”
Alternatively:
  hb ≥ 10 feet:
  hb ≥ 15 feet:
4/12/2022
Behavior of Anchored Veneer
23

## Slide 24: Behavior at Ultimate Loads
Masonry
  Multiple masonry cracks may develop
Anchors
  Load transferred at top and bottom anchors and anchors adjacent to cracks
  Stiffer anchors = higher anchor forces
4/12/2022
Behavior of Anchored Veneer
24

## Slide 25: Ultimate Load Criteria
Limit States
Loss of Veneer Stability
  Expected to be required in TMS 402-22
Anchor Failure
  Will discuss later
Backing Failure
  Design for code compliance
4/12/2022
Behavior of Anchored Veneer
25

## Slide 26: Ultimate Load Criteria - Stability
4/12/2022
Behavior of Anchored Veneer
26

## Slide 27: Ultimate Load Criteria - Stability
4/12/2022
Behavior of Anchored Veneer
27

## Slide 28: Ultimate Load Criteria - Stability
Ultimate Deflection (wind or seismic) | Service Level Deflection (0.42 wind) | Maximum Value for FS = 1.5 |  | 
 |  | hb/tsp | hb for tsp = 2-5/8 inch | hb for tsp = 3.5 inch
hb/100 | hb/240 | 67 | 14.6 ft | 19.5 ft
hb/150 | hb/360 | 100 | 21.9 ft | 29.2 ft
hb/200 | hb/480 | 133 | 29.1 ft | 38.8 ft
hb/250 | hb/600 | 167 | 36.5 ft | 48.7 ft
4/12/2022
Behavior of Anchored Veneer
28

## Slide 29: Ultimate Load Criteria - Stability
Anchors can provide a restoring force to maintain veneer stability.
R
4/12/2022
Behavior of Anchored Veneer
29

## Slide 30: Agenda
Behavior of Anchored Veneers
Code Requirements
Prescriptive Design
Alternative Design
  Full Engineered Method
  Tributary Area Method

## Slide 31: 2018 International Building Code
1402.3 Structural
  Designed and constructed to resist Chapter 16 loads
1403.4 Masonry
  “Masonry units, mortar, and metal accessories used in anchored and adhered veneer shall meet the physical requirements of Chapter 21.”
4/12/2022
Code Requirements for Anchored Veneer
31

## Slide 32: 2018 International Building Code
1404.2 Weather protection
  Table 1404.2 Minimum thickness of weather coverings:
    Natural Stone: 2 in.
    Architectural cast stone: 1 ¼ in.
    Other: 2 in.
1404.4.2 addresses flashing and weep holes
4/12/2022
Code Requirements for Anchored Veneer
32

## Slide 33: 2018 International Building Code
1404.6 References TMS 402 for anchored veneer design.
4/12/2022
Code Requirements for Anchored Veneer
33

## Slide 34: 2018 International Building Code
Chapter 16
  Table 1604.3 Deflection limits
  1609.1.1 References ASCE 7 for wind loads
  1613.1 References ASCE 7 for seismic loads
4/12/2022
Code Requirements for Anchored Veneer
34

## Slide 35: 2018 International Building Code
fThe wind load shall be permitted to be taken as 0.42 times the “component and cladding” load or directly calculated using the 10-year mean return interval wind speed for the purpose of determining deflection limits in Table 1604.3. Where framing members support glass, the deflection limit therein shall not exceed that specified in Section 1604.3.7.
Table 1604.3
Deflection Limits
4/12/2022
Code Requirements for Anchored Veneer
35
Construction | L or Lr | S or Wf | D + L
Exterior Walls: |  |  | 
With Plaster or stucco finishes | - | l/360 | -
With other brittle finishes | - | l/240 | -
With flexible finishes | - | l/120 | -

## Slide 36: A Digression
A digression on wind loads and deflection limits
Code or Standard | Deflection Limit | Recurrence Interval
IBC 2018 | l/240 | 10 years
BIA Technical Note 28B | l/600 | 50 years
AISI CF03-1 | l/600 | 10 years
WSCPA Brick Veneer on Steel Studs Guide | l/360 – 1/8" | 10 years
4/12/2022
Code Requirements for Anchored Veneer
36

## Slide 37: 2018 International Building Code
Chapter 21 Masonry
  2101 General
    2101.2.1 directs user back to Chapter 14 for design of veneers.
4/12/2022
Code Requirements for Anchored Veneer
37

## Slide 38: 2018 International Building Code
2103 Materials
  2103.1 Masonry units
    Concrete, clay, and stone per TMS 602 Article 2.3
    Architectural cast stone per ASTM C1364 and TMS 504
  2103.2 Mortar
    TMS 602 Articles 2.1 and 2.6 A.
  2103.4 Metal reinforcement and accessories
4/12/2022
Code Requirements for Anchored Veneer
38

## Slide 39: 2018 International Building Code
2103 Materials
  2103.2 Mortar
    TMS 602 Articles 2.1 and 2.6 A.
  2103.4 Metal reinforcement and accessories
    TMS 602 Article 2.4.
4/12/2022
Code Requirements for Anchored Veneer
39

## Slide 40: ASCE 7-16 – Minimum Design Loads
Chapter 13: Seismic Design Requirements for Nonstructural Components
Chapter 30: Wind Loads – Components and Cladding
4/12/2022
Code Requirements for Anchored Veneer
40

## Slide 41: ASCE 7-16 – Minimum Design Loads
4/12/2022
Code Requirements for Anchored Veneer
41
Seismic Loads:

## Slide 42: ASCE 7-16 – Minimum Design Loads
4/12/2022
Code Requirements for Anchored Veneer
42
Special Notes on Wind Loads
Tributary area – Use (ASCE 7 C26.2)
Parapets – Use ASCE 7 Figure 30.8-1

## Slide 43: TMS 402/602 - 16
4/12/2022
Code Requirements for Anchored Veneer
43

## Slide 44: TMS 402-16
Organization of Chapter 12
12.1 General
12.2 Anchored Veneer
  12.2.1 Alternate (Rational) Design
  12.2.2 Prescriptive
12.3 Adhered Veneer
4/12/2022
Code Requirements for Anchored Veneer
44

## Slide 45: TMS 402-16
12.1 General
  Not required to define or test f’m
  Reinforcement required for masonry not laid in running bond
    Area = 0.00028 x gross vertical area
    Max spacing = 48 in.
4/12/2022
Code Requirements for Anchored Veneer
45

## Slide 46: TMS 402-16
12.1 General
  Not required to define or test f’m
  12.1.4 excludes anchored dimension stone from provisions (expected to be included in TMS 402-22)
  12.1.6
    Addresses control of water
    Design and detail veneer to accommodate differential movement.
4/12/2022
Code Requirements for Anchored Veneer
46

## Slide 47: TMS 602-16
Article 2.1 Mortar
  ASTM C270
Article 2.3 Masonry units
  Concrete, clay and stone units – numerous ASTM’s
  Reminder:
    Cast stone per IBC (no conflict)
    Stone outside of Chapter 12
4/12/2022
Code Requirements for Anchored Veneer
47

## Slide 48: TMS 602-16
Article 2.4 Reinforcement, prestressing tendons, and metal accessories
  Reinforcement for veneer not laid in running bond.
      Single wire
      Same cold-worked wire as joint reinforcement
      Knurled like joint reinforcement longitudinal wires
  Includes requirements for anchors
4/12/2022
Code Requirements for Anchored Veneer
48

## Slide 49: Quality Assurance
Table 3 – Verification
  Prior to construction, verification of compliance of submittals.
Table 4 – Special Inspection
  Only required in Risk Category IV
  Design professional can choose to exceed these minimums
4/12/2022
Code Requirements for Anchored Veneer
49
TMS 402
TMS 602

## Slide 50: Agenda
Behavior of Anchored Veneers
Code Requirements
Prescriptive Design
Alternative Design
  Full Engineered Method
  Tributary Area Method

## Slide 51: Prescriptive Design
General Requirements
Most anchored veneers are constructed using this method
Based on historical practice, not engineering.
Provides maximum anchor spacing, based on:
  Wind pressure, qh
  Seismic Design Category
  Anchor Type
4/12/2022
Prescriptive Design of Anchored Veneers
51

## Slide 52: Prescriptive Design - Limitations
Limitations Loads
Wind loads
  Velocity pressure, qz ≤ 55 psf (12.2.2.1, 12.2.2.12)
  If qz > 40 psf, Mean roof height, h ≤ 60 feet (12.2.2.12)
Seismic Loads – No limit
4/12/2022
Prescriptive Design of Anchored Veneers
52

## Slide 53: Prescriptive Design - Limitations
Limitations - Geometric
Cavity 6 5/8” maximum
  Note special requirements when cavity > 4 5/8”
Air Space 1” minimum
Unit Thickness
  Unit thickness ≥ 2 5/8” (12.2.2.3.1)
  Note: Controls over IBC minimum thickness for weather protection
4/12/2022
Prescriptive Design of Anchored Veneers
53
Image from imiweb.org

## Slide 54: Prescriptive Design - Supports
Supported on non-combustible construction (12.2.2.3.1). Exceptions:
  Exterior ≤ 12’ of veneer weighing ≤ 40 psf. (12.2.2.3.1.2)
  Interior ≤ 40 psf (12.2.2.3.1.3)
Construction supporting supports must also be non-combustible. (12.2.2.3.2)
Deflections of supports under dead + live ≤ l/600. (12.2.2.3.3)
4/12/2022
Prescriptive Design of Anchored Veneers
54

## Slide 55: Prescriptive Design - Anchors
Adjustable Anchors (12.2.2.5.5)
Adjustable
Adjustable by 1 ¼”
Max 1/16” clearance
Construction prescribed
Used with all backing types
One anchor for 2.67 ft2
  Wind > 40 psf: 1.87 ft2
  Seismic D+: 2.00 ft2
4/12/2022
Prescriptive Design of Anchored Veneers
55
Adjustable

## Slide 56: Prescriptive Design - Anchors
Wire and Joint Reinforcement Anchors
Prescriptive wire size
Used with masonry backing
One anchor for 3.50 ft2
  Wind > 40 psf: 2.45 ft2
  Seismic D+: 2.62 ft2
Joint Reinforcing
4/12/2022
Prescriptive Design of Anchored Veneers
56

## Slide 57: Prescriptive Design - Anchors
Corrugated
Corrugated Anchors
Wood backing only
1” max space to sheathing
Consider ring shanked nail in lieu of common nail allowed by TMS 402.
4/12/2022
Prescriptive Design of Anchored Veneers
57

## Slide 58: Prescriptive Design - Anchors
Anchor Spacing (12.2.2.5.6)
Adjustable two-piece anchors, anchors of wire size W1.7 provide at least one anchor for each 2.67 ft2 of wall area.
Spacing not to exceed 32” horizontally and 25” vertically
Additional anchors around openings.
4/12/2022
Prescriptive Design of Anchored Veneers
58

## Slide 59: Prescriptive Design - Anchors
Anchor Spacing
Seismic Design Category D+ (12.2.2.11.2.2)
  Reduce area supported by ties to 75%
High Wind: qz > 40 psf (12.2.2.3.1)
  Reduce area supported by ties to 70%
  18” max tie spacing
  Tighter tie spacing around openings
4/12/2022
Prescriptive Design of Anchored Veneers
59

## Slide 60: Prescriptive Design - Backing
Clay, concrete, or cast stone units
Anchors and Fastening of anchors to backing
  See 12.2.2.5
Steel studs must be corrosion resistant and have minimum thickness of 0.043 in. (12.2.2.7.4)
4/12/2022
Prescriptive Design of Anchored Veneers
60

## Slide 61: Prescriptive Design - Backing
Backing types addressed:
Wood (12.2.2.6)
Steel (12.2.2.7)
Concrete (12.2.2.8)
Masonry (12.2.2.9)
4/12/2022
Prescriptive Design of Anchored Veneers
61

## Slide 62: Prescriptive Design – Wood Backing
Wood backing – height of veneer cannot exceed 30’ (38’ at gable) above support (12.2.2.6.1)
Requirements for fastening anchor to wood (12.2.2.6.3)
4/12/2022
Prescriptive Design of Anchored Veneers
62

## Slide 63: Prescriptive Design – Steel Backing
Steel studs must be corrosion resistant and have minimum thickness of 0.043 in. (12.2.2.7.4)
Steel backing if height of anchored veneer exceeds 30’ (38’ at gable) above support, must support at each floor above 30’. (12.2.2.7.1)
Requirements for fastening anchor to steel (12.2.2.7.3)
4/12/2022
Prescriptive Design of Anchored Veneers
63

## Slide 64: Not Laid In Running Bond
Not Laid in Running Bond requires at least one W1.7 wire, at 18” oc vertically. (12.2.2.10)
Must also comply with Section 4.5 – will control when veneer thickness exceeds 3-3/8 in.
4/12/2022
Prescriptive Design of Anchored Veneers
64

## Slide 65: Agenda
Behavior of Anchored Veneers
Code Requirements
Prescriptive Design
Alternative Design
  Full Engineered Method
  Tributary Area Method

## Slide 66: Code Requirements
Alternate Design Requirements
12.2.1 Alternative design . . . shall satisfy the following conditions:
(a) Loads shall be distributed through the veneer to the anchors and the backing using principles of mechanics.
(b) Out-of-plane deflection of the backing shall be limited to maintain veneer stability.
4/12/2022
Alternative Design of Anchored Veneer
66

## Slide 67: Code Requirements
Alternate Design Requirements
(c) The veneer is not subject to the flexural tensile stress provisions of Section 8.2 or the nominal flexural tensile strength provisions of Section 9.1.9.2.
(d) The provisions of Section 12.1, Section 12.2.2.10, and Section 12.2.2.11 shall apply.
4/12/2022
Code Requirements for Anchored Veneer
67

## Slide 68: Code Requirements
Alternate Design Requirements
12.1.6.3 Design and detail the veneer to accommodate differential movement.
12.2.10 Not in Running Bond – reinforcing of veneer required:
Not Laid in Running Bond requires at least one W1.7 wire, at 18” oc vertically. (12.2.2.10)
Note: SDC based requirement for reinforcing is no longer in TMS 402.
4/12/2022
Code Requirements for Anchored Veneer
68

## Slide 69: Code Requirements
Alternate Design Requirements
12.2.11 High Seismic
C+: Isolate sides and top of veneer
D+: Reduce area supported by ties to 75%, fasteners to wood (????)
E+: Support veneer at every floor
4/12/2022
Code Requirements for Anchored Veneer
69

## Slide 70: Code Requirements
Alternate Design Commentary
12.1.1 Commentary
. . .the designer should consider the following conditions and assumptions:
The veneer may crack in flexure under allowable stress level loads.
Deflection of the backing should be limited to control crack width in the veneer and to provide veneer stability.
4/12/2022
Code Requirements for Anchored Veneer
70

## Slide 71: Code Requirements
Alternate Design Commentary
Connections of the anchor to the veneer and to the backing should be sufficient to transfer applied loads.
Differential movement should be considered in the design, detailing, and construction.
Water will penetrate the veneer, and the wall system should be designed, detailed, and constructed to prevent water penetration into the building.
4/12/2022
Code Requirements for Anchored Veneer
71

## Slide 72: Code Requirements
Alternate Design Commentary
Requirements for corrosion protection and fire resistance must be included.
4/12/2022
Code Requirements for Anchored Veneer
72

## Slide 73: Agenda
Behavior of Anchored Veneers
Code Requirements
Prescriptive Design
Alternative Design
  Full Engineered Method
  Tributary Area Method

## Slide 74: Full Engineered Method
Suggested Procedure
Determine Loads
Design Backing
Check Stability
Select Anchor Type
Estimate Anchor Spacing
Pseudo-Nonlinear Analysis
Verify Anchor Demands
4/12/2022
Alternative Design of Anchored Veneer
74

## Slide 75: Modeling Anchored Veneer
Image from imiweb.org
4/12/2022
Full Engineered Design of Anchored Veneer
75

## Slide 76: Modeling - Masonry
Masonry Component Behavior
Cracking Allowed – Model Non-Linear Behavior
Material Properties
  Elastic Stiffness
  Cracking strength
4/12/2022
Full Engineered Design of Anchored Veneer
76

## Slide 77: Masonry – Material Properties
Elastic stiffness (EI)
  Elastic Modulus per TMS 402 :
    Concrete Masonry
    Clay Masonry
    Cast Stone (expected in TMS 402-22)
    Dimension stone not addressed
4/12/2022
Full Engineered Design of Anchored Veneer
77

## Slide 78: Masonry – Determining f’m
Clay and concrete units, can use unit strength method to determine f’m
Clay
Concrete
For veneers, unit strength may be unknown.
4/12/2022
Full Engineered Design of Anchored Veneer
78

## Slide 79: Masonry – Determining f’m
Cast stone
  Minimum unit strength = 6,500 psi (ASTM C1364)
  Prism test to determine f’m
Dimension stone
  Not addressed, presumably prism test
4/12/2022
Full Engineered Design of Anchored Veneer
79

## Slide 80: Masonry – Material Properties
Cracking strength (frS)
  Thickness of units (S)
  Modulus of Rupture (fr)
For veneers, Type N Mortar is typically preferred.
4/12/2022
Full Engineered Design of Anchored Veneer
80

## Slide 81: Anchor Properties
Assume linear elastic behavior, need:
Stiffness
Strength
4/12/2022
Full Engineered Design of Anchored Veneer
81

## Slide 82: Anchor Properties
Anchor Component Behavior
Images from “Masonry Anchors and Ties by the Code,” Paul Curtis, Masonry.
4/12/2022
Full Engineered Design of Anchored Veneer
82

## Slide 83: Anchor Properties
Adjustable
Adjustable – 2 Leg
Adjustable by 1 ¼”
Properties vary based on position
1/16” free play
Used with all backing types
4/12/2022
Full Engineered Design of Anchored Veneer
83

## Slide 84: Anchor Properties
Limit States for Adjustable 2-Leg Anchors
Pull Out / Push Through at the Mortar Joint
Failure within Anchor
  Buckling
  Tension yielding
  Tension rupture
  Flexural yielding
Failure of Fastener to Backing
Adjustable
4/12/2022
Full Engineered Design of Anchored Veneer
84

## Slide 85: Anchor Properties
Sources of Information on Anchor Behavior
Adjustable
Manufacturers
Research
  “Proposed Changes to the TMS 402 Anchored Veneer Provisions”, Hochwalt, Bennett, et al, Proceedings of the 13th North American Masonry Conference, 2019.
  Mostly Bennett
4/12/2022
Full Engineered Design of Anchored Veneer
85

## Slide 86: Anchor Properties
Cautions on Manufacturer Data
Adjustable
No standard for anchor testing in US
Tests often do not consider mortar or fastener failure modes
Are tests compliant with IBC 1709?
4/12/2022
Full Engineered Design of Anchored Veneer
86

## Slide 87: Anchor Properties
How wide was cavity?
What position was anchor in for compression testing?
Use the mean test value? Apply some statistical analysis?
What factor of safety should be applied?
Was mortar joint pull out / push through tested?
Example Manufacturer Data
4/12/2022
Full Engineered Design of Anchored Veneer
87

## Slide 88: Anchor Properties
What factor of safety should be applied?
Is the anchor stiffness = plateau displacement divided by the failure load?
Example Manufacturer Data
4/12/2022
Full Engineered Design of Anchored Veneer
88

## Slide 89: Anchor Properties
Working Load provided
  Based on deflection limit
  What factory of safety does this represent?
  What if you want to design for ultimate loads?
How many tests were done?
Was mortar joint tested?
Example Manufacturer Data
4/12/2022
Full Engineered Design of Anchored Veneer
89

## Slide 90: Behavior of Anchored Veneers
Anchor Component Behavior
Generic Properties for Adjustable 2-Leg Anchors
From Hochwalt, Bennett et al (2019)
Use for design strength, lesser of
  0.5 x average ultimate strength in mid—point of adjustment
  1.5 x the strength in the position of maximum offset
Allowable load = 0.6 x design strength.
Stiffness typically not reported very well. Ideally use the secant stiffness between 10 lbs and 40% of ultimate in mid-point position.
4/12/2022
Full Engineered Design of Anchored Veneer
90

## Slide 91: Backing Properties
Backing Component Behavior
Material Properties
  Steel Studs (AISI)
  Wood Studs (NDS)
  Concrete Wall (ACI 318)
  Masonry Wall (TMS 402)
Serviceability Criteria - Deflection
Limit State - Strength
4/12/2022
Full Engineered Design of Anchored Veneer
91

## Slide 92: Full Engineered Method - Example
Suggested Procedure
Determine Loads
Design Backing
Check Stability
Select Anchor Type
Estimate Anchor Spacing
Pseudo-Nonlinear Analysis
Verify Anchor Demands
4/12/2022
Full Engineered Design of Anchored Veneer
92

## Slide 93: Full Engineered Design
Givens:
60’-0” building height
12’-0” story height
qz = 28 psf
Component and Cladding Pressure = 45 psf
Seismic Design Category = D
  Veneer, Connection Body = 11 psf
  Fasteners = 35 psf
4/12/2022
Full Engineered Design of Anchored Veneer
93

## Slide 94: Full Engineered Design
Givens:
3 ½” clay units
Type N mortar cement mortar
6” steel studs at 16” on center
Goal:
Maximize energy performance by maximizing anchor spacing
4/12/2022
Full Engineered Design of Anchored Veneer
94

## Slide 95: Full Engineered Method
Suggested Procedure
Determine Loads
Design Backing
Check Stability
Select Anchor Type
Estimate Anchor Spacing
Pseudo-Nonlinear Analysis
Verify Anchor Demands
4/12/2022
Full Engineered Design of Anchored Veneer
95

## Slide 96: Full Engineered Design
Design Backing:
Determine target deflection. For adjustable anchors:
Determine required moment of inertia:
4/12/2022
Full Engineered Design of Anchored Veneer
96

## Slide 97: Full Engineered Design
Design Backing:
Use 10 year wind:
Solve for Imin:
=
  Note that this is per foot. For 16” spacing, Imin = 1.33(1.09) = 1.46 in4
4/12/2022
Full Engineered Design of Anchored Veneer
97

## Slide 98: Full Engineered Design
Design Backing:
Consult SSMA Manual:
  Looks like 600S137-33 might work
4/12/2022
Full Engineered Design of Anchored Veneer
98

## Slide 99: Full Engineered Design
Design Backing:
Check allowable moment:
  Still looks like 600S137-33
4/12/2022
Full Engineered Design of Anchored Veneer
99

## Slide 100: Full Engineered Design
Design Backing:
  Fasteners
    For prescriptive designs 12.2.2.7.4 requires min thickness of 0.043 in (43 mil)
    BIA Technical Note 28B also recommends 43 mil minimum
    We’re going to use slotted anchors
      200 lb allowable load
      (2) screws; need 100 lbs per screw
4/12/2022
Full Engineered Design of Anchored Veneer
100

## Slide 101: Full Engineered Design
Design Backing:
  Use 600S137-43.
  Note I = 2.042 in4
4/12/2022
Full Engineered Design of Anchored Veneer
101

## Slide 102: Full Engineered Method
Suggested Procedure
Determine Loads
Design Backing
Check Stability
Select Anchor Type
Estimate Anchor Spacing
Pseudo-Nonlinear Analysis
Verify Anchor Demands
4/12/2022
Full Engineered Design of Anchored Veneer
102

## Slide 103: Full Engineered Method
Check Stability
4/12/2022
Full Engineered Design of Anchored Veneer
103

## Slide 104: Full Engineered Method
Check Stability
Deflection of Backing |  | Maximum value for deemed to comply |  | 
Wind1 | Seismic2 | hb/tsp | hb for tsp = 2-5/8 inch | hb for tsp = 3.5 inch
hb/240 | hb/100 | 67 | 14.6 ft | 19.5 ft
hb/360 | hb/150 | 100 | 21.9 ft | 29.2 ft
hb/480 | hb/200 | 133 | 29.1 ft | 38.8 ft
hb/600 | hb/250 | 167 | 36.5 ft | 48.7 ft
1Under application of 0.42 times the strength level wind load.
2Under application of the strength level seismic load.
12’ height is OK
4/12/2022
Full Engineered Design of Anchored Veneer
104

## Slide 105: Full Engineered Method
Suggested Procedure
Determine Loads
Design Backing
Check Stability
Select Anchor Type
Estimate Anchor Spacing
Pseudo-Nonlinear Analysis
Verify Anchor Demands
4/12/2022
Full Engineered Design of Anchored Veneer
105

## Slide 106: Full Engineered Method
Adjustable
Select Anchor Type
  Design Strength:
  330 lbs
  Allowable Load:
  200 lbs
  Stiffness:
  3,000 lb/in
Slotted Anchors
Want adjustable anchor to accommodate expansion of brick.
Slotted anchor has higher capacity than 2-Leg anchors
4/12/2022
Full Engineered Design of Anchored Veneer
106

## Slide 107: Full Engineered Method
Suggested Procedure
Determine Loads
Design Backing
Check Stability
Select Anchor Type
Estimate Anchor Spacing
Pseudo-Nonlinear Analysis
Verify Anchor Demands
4/12/2022
Full Engineered Design of Anchored Veneer
107

## Slide 108: Full Engineered Design
Estimate Anchor Spacing:
Transverse spacing = stud spacing
Longitudinal spacing
  Tributary Area Method
  Prescriptive Method
4/12/2022
Full Engineered Design of Anchored Veneer
108

## Slide 109: Full Engineered Design
Estimate Anchor Spacing:
Prescriptive Method
  Adjustable Anchors
    One anchor per 2.67 ft2 (12.2.2.5.6.1)
    Horizontal 32” max (12.2.2.5.6.3)
    Vertical 25” max (12.2.2.5.6.3)
  High Wind? No. qz < 40 psf (12.2.2.12)
  High Seismic? Yes. SDC D (12.2.2.12)
    Reduce max area to 75%
4/12/2022
Full Engineered Design of Anchored Veneer
109

## Slide 110: Full Engineered Design
Estimate Anchor Spacing:
Prescriptive Method
  Area per anchor = 0.75 x 2.67 = 2.00 ft2
  Horizontal spacing = stud spacing = 16”
  Vertical spacing = 2.00 / 1.33 = 18”
    Masonry module is 8”, we would use 16”
4/12/2022
Full Engineered Design of Anchored Veneer
110

## Slide 111: Full Engineered Design
Estimate Anchor Spacing:
Since prescriptive method would require 16” spacing, try for 32” vertical spacing.
4/12/2022
Full Engineered Design of Anchored Veneer
111

## Slide 112: Full Engineered Method
Suggested Procedure
Determine Loads
Design Backing
Check Stability
Select Anchor Type
Estimate Anchor Spacing
Pseudo-Nonlinear Analysis
Verify Anchor Demands
4/12/2022
Full Engineered Design of Anchored Veneer
112

## Slide 113: Full Engineered Method
Model Properties
Backing
  EI known for 600S137-43 studs
Anchors
  Slotted anchors = 3,000 lb/in
Masonry
  Stiffness, EmI
    Need elastic modulus, Em
  Strength, Mcr = frS
    Need modulus of rupture, fr
4/12/2022
Full Engineered Design of Anchored Veneer
113

## Slide 114: Full Engineered Method
Model Properties
  Elastic Modulus
    Concrete Masonry
    Clay Masonry
  f’m is per Unit Strength Method in TMS 602
    Need unit strength
    May be unknown
4/12/2022
Full Engineered Design of Anchored Veneer
114

## Slide 115: Full Engineered Method
Model Properties
BIA Technical Note 3A
4/12/2022
Full Engineered Design of Anchored Veneer
115

## Slide 116: Full Engineered Method
Model Properties
Assume f’m = 2,500 psi
4/12/2022
Full Engineered Design of Anchored Veneer
116

## Slide 117: Full Engineered Method
Model Properties
4/12/2022
Full Engineered Design of Anchored Veneer
117

## Slide 118: Full Engineered Method
Model Creation
Pseudo-Nonlinear
  Manually insert hinges at cracks
  Could do true nonlinear
Anchors
  Modeled as axial elements
4/12/2022
Full Engineered Design of Anchored Veneer
118

## Slide 119: Full Engineered Method
Model Analysis
Apply ultimate load to model
Veneer is uncracked
Max moment at midheight = 8.02 in-k
  Exceeds cracking moment = 3.27 in-k
  First crack will occur at midheight
  Crack expected at (3.27/8.02) 45 psf = 18.3 psf
4/12/2022
Full Engineered Design of Anchored Veneer
119

## Slide 120: Full Engineered Method
Model Analysis
Insert hinge at midheght to represent first crack
Max moment = 6.55 in-k
  Exceeds cracking moment = 3.27 in-k
  Crack expected at (3.27/6.55) 45 psf = 22.5 psf
4/12/2022
Full Engineered Design of Anchored Veneer
120

## Slide 121: Full Engineered Method
Model Analysis
Insert second hinge to represent second crack
Max moment = 3.49 in-k
  Exceeds cracking moment = 3.27 in-k
  Crack expected at (3.27/3.49) 45 psf = 42.2 psf
4/12/2022
Full Engineered Design of Anchored Veneer
121

## Slide 122: Full Engineered Method
Model Analysis
Insert third hinge to represent third crack
Max moment = 1.59 in-k
  Less than cracking moment = 3.27 in-k
  Condition at ultimate load has been determined
4/12/2022
Full Engineered Design of Anchored Veneer
122

## Slide 123: Full Engineered Method
Model Analysis
Extract anchor forces
Max anchor force 208 lbs < 330 anchor capacity OK
Max anchor has effective tributary area:
  208 lbs / 45 psf = 4.62 ft2
  Physical area = 1.33 x 2.67 = 3.55
  Effective tributary area = 4.62 / 3.55 = 1.3 physical tributary area
130 lbs
191 lbs
175 lbs
208 lbs
81 lbs
4/12/2022
Full Engineered Design of Anchored Veneer
123

## Slide 124: Full Engineered Method
Point of Curiosity #1
Veneer: not considered to add strength or stiffness to the wall system
Ultimate loads
  Max moment in backing
    Without veneer = 13.0 k-in
    With veneer = 13.4 k-in
  Max deflection of backing
    Without veneer = 0.47 in
    With veneer = 0.51 in
4/12/2022
Full Engineered Design of Anchored Veneer
124

## Slide 125: Full Engineered Method
Point of Curiosity #2
Veneer: not considered to add strength or stiffness to the wall system
ASD loads
  Max moment in backing
    Without veneer = 7.78 k-in
    With veneer = 8.84 k-in
  Max deflection of backing
    Without veneer = 0.28 in
    With veneer = 0.26 in
Assumes no previous load causing third crack
4/12/2022
Full Engineered Design of Anchored Veneer
125

## Slide 126: Full Engineered Method
Point of Curiosity #3
Veneer: not considered to add strength or stiffness to the wall system
10 Year load
  Max moment in backing
    Without veneer = 5.44 k-in
    With veneer = 6.15 k-in
  Max deflection of backing
    Without veneer = 0.20 in
    With veneer = 0.15 in
Assumes no previous load causing second crack
4/12/2022
Full Engineered Design of Anchored Veneer
126

## Slide 127: Agenda
Behavior of Anchored Veneers
Code Requirements
Prescriptive Design
Alternative Design
  Full Engineered Method
  Tributary Area Method

## Slide 128: Tributary Area Method
Full Engineered Method is a lot of work
Is there an easier way?
Could we develop an equivalent tributary area?
4/12/2022
Tributary Area Design of Anchored Veneer
128

## Slide 129: Tributary Area Method
Scenario 1:
Flexible anchors
Single crack at midheight
Center anchor takes maximum load:
  Fp = 0.5(Astud)(pressure)
  Or, as illustrated
  Fp = 3(Atrib)(pressure)
4/12/2022
Tributary Area Design of Anchored Veneer
129

## Slide 130: Tributary Area Method
Scenario 2:
Masonry cracked at each anchor
Load on anchor is just based on the physical tributary area of the anchor:
  Fp = (Atrib)(pressure)
4/12/2022
Tributary Area Design of Anchored Veneer
130

## Slide 131: Tributary Area Method
Source | Required Anchor Strength
UBC (1997) Section 1403.4.3 | Twice veneer weight of At
WSCPA (2004) | Anchor Force: Ta = 0.25pAstud Ultimate capacity: 1.25Ta if k ≤ 2000 lb/in. (350 N/mm) 2.0Ta if k > 2000 lb/in. (350 N/mm)
AISI (2014), CSSBI (2008) | 0.4pAstud, but not less than 2pAt
McGinley (2010) | Stud backed system with stiff anchors: 0.25pAstud Flexible/ductile anchor systems with stiff backing: pAt
CSA S304.1 (2014) | Flexible backing (stiffness ≤ 2.5 uncracked veneer stiffness): 0.4pAstud, but not less than 2pAt Stiff backing: pAt
AS 3700 (2011) | Flexible backing (stiffness ≤ 0.5 uncracked veneer stiffness): 0.2pAstud; 0.4pAstud top row (can use stronger anchor, or double number of anchors) Stiff backing: 1.3pAt
Note: Ta = anchor force; p = design pressure (either wind or earthquake); At = tributary area; Astud = tributary area of stud (stud spacing × stud height); k = stiffness of anchor
“Proposed Changes to the TMS 402 Anchored Veneer Provisions”, Hochwalt, Bennett, et al, Proceedings of the 13th North American Masonry Conference, 2019.
4/12/2022
Tributary Area Design of Anchored Veneer
131

## Slide 132: Tributary Area Method
Parametric Study:
144 Pseudo non-linear analyses (Bennett)
  Looked at varying:
  Masonry stiffness and strength
  Tie stiffness
  Backing stiffness
Tie stiffness was most critical factor
4/12/2022
Tributary Area Design of Anchored Veneer
132

## Slide 133: Tributary Area Method
4/12/2022
Tributary Area Design of Anchored Veneer
133

## Slide 134: Tributary Area Method
Suggested Values
Tie Stiffness | Tie Force
ktie ≤ 2500 lb/in. | 2.0puAt
2500 lb/in. < ktie ≤ 5000 lb/in. | 2.5puAt
5000 lb/in. < ktie ≤ 8000 lb/in. | 3.0puAt
ktie > 8000 lb/in. | 4.0puAt
4/12/2022
Tributary Area Design of Anchored Veneer
134

## Slide 135: Tributary Area Method
Givens:
60’-0” building height
12’-0” story height
qz = 28 psf
Component and Cladding Pressure = 45 psf
Seismic Design Category = D
  Veneer, Connection Body = 11 psf
  Fasteners = 35 psf
4/12/2022
Tributary Area Design of Anchored Veneer
135

## Slide 136: Tributary Area Method
Givens:
3 ½” clay units
Type N mortar cement Mortar
6” steel studs at 16” on center
Goal:
Maximize energy performance by maximizing anchor spacing
4/12/2022
Tributary Area Design of Anchored Veneer
136

## Slide 137: Tributary Area Method
Suggested Procedure
Determine Loads – Same as Full Engineered
Design Backing – Same as Full Engineered
Check Stability – Same as Full Engineered
Select Anchor Type
Determine Anchor Spacing
4/12/2022
Tributary Area Design of Anchored Veneer
137

## Slide 138: Tributary Area Method
Adjustable
Select Anchor Type
  Design Strength:
  330 lbs
  Allowable Load:
  200 lbs
  Stiffness:
  3,000 lb/in
Slotted Anchors
Want adjustable anchor to accommodate expansion of brick.
Slotted anchor has higher capacity than 2-Leg anchors
4/12/2022
Tributary Area Design of Anchored Veneer
138

## Slide 139: Tributary Area Method
Determine Anchor Spacing
Tie Stiffness | Tie Force
ktie ≤ 2500 lb/in. | 2.0puAt
2500 lb/in. < ktie ≤ 5000 lb/in. | 2.5puAt
5000 lb/in. < ktie ≤ 8000 lb/in. | 3.0puAt
ktie > 8000 lb/in. | 4.0puAt
16” x 24” Spacing
4/12/2022
Tributary Area Design of Anchored Veneer
139

## Slide 140: Tributary Area Method
Comparison of Anchor Spacings
Prescriptive: 16” x 16”
Tributary Area Method: 16” x 24”
  1/3 reduction in anchors / thermal bridging
Full Engineered Method: 16” x 32”
  1/2 reduction in anchors / thermal bridging
4/12/2022
Tributary Area Design of Anchored Veneer
140

## Slide 141: Anchored Veneer Close
Special Inspection / Quality Assurance
  Chapter 12 (veneer) is in Part 4
  Recommend treating engineered veneers as if they were in Part 3.
4/12/2022
Tributary Area Design of Anchored Veneer
141

## Slide 142: Anchored Veneer Close
  Resources
    Anchors
      BIA Technical Note 44B
      NCMA TEK 12-01B
      “Proposed Changes to the TMS 402 Anchored Veneer Provisions”, Hochwalt, Bennett, et al, Proceedings of the 13th North American Masonry Conference, 2019
4/12/2022
Tributary Area Design of Anchored Veneer
142

## Slide 143: Anchored Veneer Close
    Concrete Masonry Backing
      BIA Technical Note 28
    Concrete Masonry Veneers
      NCMA TEK 03-06C
      NCMA TEK 05-02A
    Jointing of Veneers
      BIA Technical Note 18A
      NCMA TEK 10-04
4/12/2022
Tributary Area Design of Anchored Veneer
143

## Slide 144: Anchored Veneer Close
    Lintels
      BIA Technical Note 31B
      Tide, R.H.R and N.V. Krogstad, 1993, “Economical Design of Shelf Angles,” Proceedings of the Symposium on Masonry: Design and Construction, Problems and Repair, STP 1180, American Society for Testing and Materials, Philadelphia, PA.
    Steel Stud Backing
      AISI Brick Veneer Cold-Formed Steel Framing Design Guide
      BIA Technical Note 28B
      WSCPA “Design Guide for Anchored Brick Veneer over Steel Studs” Available now at www.brick-wscpa.org
4/12/2022
Tributary Area Design of Anchored Veneer
144

## Slide 145: Anchored Veneer Close
    Steel Stud Backing (continued)
      “Addressing Maximum Design Deflection for Cold-Formed Steel Framing When Used as a Backing for Brick Veneer ”, Clark, Fried, Byra, Masonry 2018, ASTM STP1612, 2018.
    Structural Brick Veneer
      BIA Technical Note 41
      WSCPA “Design Guide for Structural Brick Veneer”
    Wood Stud Backing
      BIA Technical Note 28
      BIA, Brick Brief, “Designing Anchored Brick Veneer Above 30 Feet with a Backing of Wood Framing”, 2015.
      Wood Products Council, “Options for Brick Veneer on Mid-Rise Wood-Frame Buildings”, 2015.
4/12/2022
Tributary Area Design of Anchored Veneer
145

## Slide 146: Adhered Veneer

## Slide 147: Adhered Veneer Assembly
4/12/2022
Adhered Veneer
147
Image from imiweb.org

## Slide 148: Adhered Veneer Assembly
4/12/2022
Adhered Veneer
148
Image from imiweb.org

## Slide 149: Agenda
Behavior of Adhered Veneers
Code Requirements
Prescriptive Design
Alternative Design

## Slide 150: Agenda
Behavior of Adhered Veneers
Code Requirements
Prescriptive Design
Alternative Design

## Slide 151: 2018 International Building Code
1402.3 Structural
  Designed and constructed to resist Chapter 16 loads
1403.4 Masonry
  “Masonry units, mortar, and metal accessories used in anchored and adhered veneer shall meet the physical requirements of Chapter 21.”
4/12/2022
Code Requirements for Adhered Veneer
151

## Slide 152: 2018 International Building Code
1404.2 Weather protection
  Table 1404.2 Minimum thickness of weather coverings:
    Architectural cast stone: ¾ in.
    Other: ¼ in.
4/12/2022
Code Requirements for Adhered Veneer
152

## Slide 153: 2018 International Building Code
1404.10 References TMS 402 for adhered veneer provisions.
1404.10.1 Exterior adhered masonry veneer
  Water resistive barriers
  Flashing
  Clearances – at stud walls
4/12/2022
Code Requirements for Adhered Veneer
153
Image from imiweb.org

## Slide 154: 2018 International Building Code
1404.10.1.4 Lath and mortar installation
1404.10.1.5 Installation directly to masonry or concrete
4/12/2022
Code Requirements for Adhered Veneer
154
Image from imiweb.org

## Slide 155: 2018 International Building Code
Chapter 16
  Table 1604.3 Deflection limits
  1609.1.1 References ASCE 7 for wind loads
  1613.1 References ASCE 7 for seismic loads
4/12/2022
Code Requirements for Adhered Veneer
155

## Slide 156: 2018 International Building Code
fThe wind load shall be permitted to be taken as 0.42 times the “component and cladding” load or directly calculated using the 10-year mean return interval wind speed for the purpose of determining deflection limits in Table 1604.3. Where framing members support glass, the deflection limit therein shall not exceed that specified in Section 1604.3.7.
Table 1604.3
Deflection Limits
4/12/2022
Code Requirements for Adhered Veneer
156
Construction | L or Lr | S or Wf | D + L
Exterior Walls: |  |  | 
With Plaster or stucco finishes | - | l/360 | -
With other brittle finishes | - | l/240 | -
With flexible finishes | - | l/120 | -

## Slide 157: 2018 International Building Code
Chapter 21 Masonry
  2101 General
    2101.2.1 directs user back to Chapter 14 for design of veneers.
4/12/2022
Code Requirements for Adhered Veneer
157

## Slide 158: 2018 International Building Code
2103 Materials
  2103.1 Masonry units
    Concrete, clay, and stone per TMS 602 Article 2.3
    Architectural cast stone per ASTM C1364 and TMS 504
    Adhered manufactured stone veneer units per ASTM C1670
4/12/2022
Code Requirements for Adhered Veneer
158

## Slide 159: 2018 International Building Code
2103 Materials
  2103.2.4 Mortar for adhered masonry veneer
    ASTM C270 Type N or S
    ANSI A118.4 for latex modified mortar.
4/12/2022
Code Requirements for Adhered Veneer
159

## Slide 160: TMS 402/602 - 16
4/12/2022
Code Requirements for Adhered Veneer
160

## Slide 161: TMS 402-16
Organization of Chapter 12
12.1 General
12.2 Anchored Veneer
  12.2.1 Alternate (Rational) Design
  12.2.2 Prescriptive
12.3 Adhered Veneer
4/12/2022
Code Requirements for Adhered Veneer
161

## Slide 162: TMS 402-16
12.1 General
  Not required to define or test f’m
  12.1.6
    Addresses control of water
    Design and detail veneer to accommodate differential movement.
4/12/2022
Code Requirements for Adhered Veneer
162

## Slide 163: TMS 602-16
Article 2.1 Mortar
  No special reference for adhered
  Per IBC
Article 2.3 Masonry units
  Concrete, clay and stone units – numerous ASTM’s
  Reminder:
    Cast stone per IBC (no conflict)
    Adhered manufactured stone per IBC (no conflict)
4/12/2022
Code Requirements for Adhered Veneer
163

## Slide 164: Suggested for TMS 602-22
Limit backing deflection to under 0.42 strength level wind load, or under strength level seismic load.
  Limit cracking
  Maintain stability
4/12/2022
Code Requirements for Adhered Veneer
164

## Slide 165: Quality Assurance
Table 3 – Verification
  Prior to construction, verification of compliance of submittals.
Table 4 – Special Inspection
  Only required in Risk Category IV
  Design professional can choose to exceed these minimums
4/12/2022
Code Requirements for Adhered Veneer
165
TMS 402
TMS 602

## Slide 166: Agenda
Behavior of Adhered Veneers
Code Requirements
Prescriptive Design
Alternative Design

## Slide 167: Prescriptive Design – TMS 402-16
General Requirements
TMS 402-16 Provisions are outdated (1967)
Type S mortar applied directly to concrete or masonry
Most adhered veneers constructed using industry recommendations
No restrictions on use
4/12/2022
Prescriptive Design of Adhered Veneers
167

## Slide 168: Prescriptive Design – TMS 402-16
General Requirements
12.3.2.1 Unit sizes
  2-5/8” maximum thickness
  36” maximum unit dimension
  5 psf max area
  15 psf max weight
4/12/2022
Prescriptive Design of Adhered Veneers
168

## Slide 169: Prescriptive Design – TMS 402-16
12.3.2.2 Wall area limitations
  Just as required to accommodate differential movements
12.3.2.3 Backing – moisture resistant and any of:
  Masonry
  Concrete
  Lath and plaster applied to masonry, concretem steel framing, wood framing
4/12/2022
Prescriptive Design of Adhered Veneers
169

## Slide 170: Prescriptive Design – TMS 402-16
12.3.2.4 Adhesion, either:
  Shear strength of 50 psi when tested per ASTM C482, or
  Comply with TMS 602 Article 3.3 C.
    Developed in early 1950’s
    Uses Type S mortar
  How does this relate to IBC installation requirements?
4/12/2022
Prescriptive Design of Adhered Veneers
170

## Slide 171: Prescriptive Design – TMS 402-22
Expected to
  Recognize multiple types of backing
  Recognize modern setting bed mortars:
    ANSI 118.4 – Modified Dry Set Cement Mortar
      Formerly: Latex Portland Cement Mortar
    ASTM 118.15 – Improved Modified Dry-Set Cement Mortar
  Place limits on applications, including 60 feet max height.
4/12/2022
Prescriptive Design of Adhered Veneers
171

## Slide 172: Prescriptive Design – TMS 402-22
4/13/2022
Prescriptive Design of Adhered Veneers
172
Sample Table for Prescriptive Design (other than concrete or masonry backing)

## Slide 173: Agenda
Behavior of Adhered Veneers
Code Requirements
Prescriptive Design
Alternative Design

## Slide 174: Anchored Veneer Close
  Resources
    Adhered Veneers
      BIA Technical Note 28C
      “Proposed Changes to the TMS 402 Adhered Veneer Provisions”, Thompson, Clark, et al, Proceedings of the 13th North American Masonry Conference, 2019
      “Initial Design Method for Thin Masonry Veneers Individually Secured by Mortar Adhesion”, Hagel, M., Isfeld, Al., and Rizaee, S. 13th Canadian Masonry Symposium, Halifax, CA, 2017.
      Installation Guide and Detailing Options for Compliance with ASTM C1780 For Adhered Manufactured Stone Veneer 5th Edition, 4th Printing, National Concrete Masonry Association, 2020.
4/12/2022
Adhered Veneer
174

## Slide 175: Thanks!
John.Hochwalt@kpff.com